## Slide 1
Mobile Solution to Controlling Audio Networks
Investigator: Sascha Zeisberger
Supervisor: Prof. Richard Foss

## Slide 2
Goals
Create mobile solution to audio network management
Larger networks become difficult to manage from a static
position
Mobile solution will provide flexibility as to where the
control point is situated
Will be based off an existing desktop application

## Slide 3
Audio Device
Control Station
Scenario
Notes: Stadium scenario – where 2 people were required, one to test sound levels and another to change the levels, now one is needed
The one can roam around a venue and test, control and do whatever to individual PoP’s (points of presence)
Also talk about controlling multiple input devices

## Slide 4
Background
Unos Vision
  Audio network management suite
  Uses X170 Protocol
  Grid-based approach to audio networking
  Majority of device interaction is via desk items
iPhone/iPod
  Powerful smartphone
  Flexible in terms of features (touch-screen, wireless…)

## Slide 5
Unos Vision Example

## Slide 6
First Step: Straight Port
Facilitated by using the Juce framework.
XFN, Juce and Unos rebuilt for Arm.
Program once, #ifdef everywhere
Evaluation
  What features work
  Apple’s Instruments utility to measure performance
  Keystroke-Level Model to evaluate GUI

## Slide 7
Issues
Performance:
  Sluggish performance and crashes
  Sandboxed file system broke many features
Design:
  Tab-view provided better experience, but tedious to use
  Juce was new to the iPhone - resulted in odd behavior
  Controls were difficult to use

## Slide 8
Tab View

## Slide 9
Keystroke-Level Model
Predictive form of evaluation
Uses abstract representations to describe actions
Simplified version of this model was used
  C for touch/click action
  D for a drag/scroll action
  Square brackets represent optional tasks (worst-case scenarios)

## Slide 10
Keystroke-Level Model
Create connection between 2 devices on same subnet
  [D]CC[D]CC[D]CC[D]C = 11 worst, 7 best
Create connection between 2 devices on different subnets
  [D]CC[D]CC[D]C[cc[d]cc[d]c]CC[D]CC[D]CC[D]C = 25W,17B
  Number of actions = 18 + number subnets to traverse* 7

## Slide 11
Patch Bay
Patch bays abstract the complexities of routing.
Create end-to-end connections
Tree-grid based patch-bay was used
  Provides overview of network
  Easy to represent on small screens
More efficient in terms of KLM
  [D]C[D]C[D]C = 6W, 3B

## Slide 12
Keystroke-Level Model
Chart: Number of Subnets
Unos Vision | 18 | 39 | 46 | 53 | 60 | 67 | 74
Patch Bay | 6 | 6 | 6 | 6 | 6 | 6 | 6 | 6

## Slide 13
Patchbay Elements
Using Unos Vision as backend provides support for:
  Multiple instances.
  Timing and synchronization.
  Point-to-point connection creation.
Routing algorithm
  Internal routing
  Router traversal

## Slide 14
Demonstration and Questions
?
Notes: Question time.

## Slide 15
iPhone/UnosVision Template [LessContent]
Main
  Sub

## Slide 16
iPhone/UnosVision Template [XtraContent]
Main point
  Sub point